## Slide 1: NIRSCAM: A Mobile Near-Infrared Sensing System for Food Calorie Estimation Haiyan Hu, Qian Zhang, Yanjiao Chen (IOTJ 2022)

## Slide 2: Introduction
There is a pressing demand for affordable and reliable food calorie estimation systems in daily diet.
Existing solutions are expensive, complicated or unreliable.
Unreliable
Limited to superficial features
Ask for user operation
Image-based Solutions
Complicated and Bulky
Expensive
Professional Solutions
Bomb Calorimeter
Spectrometer
Can not distinguish
Give wrong calorie estimations
Food with similar appearances

## Slide 3: Observation
Near-infrared spectroscopy (NIRS) technology can detect underlying chemical characteristics of food, so that to provide reliable food nutrients and calories estimation.
Each nutrient has a distinctive near-infrared absorption spectrum

## Slide 4: NIRSCAM
We propose a low-cost mobile near-infrared sensing system for reliable food calorie estimation, named NIRSCAM.
NIRCAM uses off-the-shelf cheap LEDs and photodiodes components to reduce the cost
Challenges:
C1: Low signal-to-noise ratio
C2: Heterogeneous of Foods
Low emission power
Ambient light noise
NIRSCAM

## Slide 5: NIRSCAM
It improves the signal quality of the system by a series of schemes, including hardware modulation and denoising algorithms
It exploits non-linear machine learning model is used to realize accurate estimations of calories.
To improve the signal quality of low-cost system
To fit the heterogeneous types of foods

## Slide 6: Evaluation
NIRSCAM is 15.32% more accurate in calorie estimation than the image-based baseline over 25 types of food.
NIRSCAM can differentiate foods with strong resemblance and gives accurate calorie estimation, like cola and diet cola.